QUICK SETUP FOR DES-6300 WITH CONFIGMASTER 8.426

- Check version of the device upon booting up. Latest Version 3.135

- Upgrade device firmware version to the latest release

- To perform a factory reset to the switch. Follow the procedures are shown below :

- Using a pc, run a terminal emulation program, e.g Hyperterminal with settings

Bits per second – 115200

Data bits – 8

Parity – None

Stop bits -1

Flow Control – None

- Issue command -> debug, followed by password dlinkdebug once prompted

- Follow by command erase cdb, once entered the system will reset.

- Once rebooted, under the > prompt, enter initerm

- As shown above, no settings are entered. Hence, configure IP address, subnet mask, port and the rest of the parameters accordingly. Note :- All ports belong to one VLAN (vid = 1) port setting 100000

- Switch reset automatically upon confirming configuration